## Slide 1: Electromagnets and their uses
Your Learning objectives:
To learn how to draw the magnetic field around a straight current-carrying wire.
To understand how to create an electromagnet.

## Slide 2
Starter
The average train journey from London to Manchester is 2 hours 45 minutes.
  Draw the free body diagram of the train travelling at a constant speed.
  How could we reduce the travel time between Manchester and London? Refer to the forces acting on the train.

## Slide 3
Answer
The train is being driven by the engine,
creating a thrust.
As the train travels faster, the force of
friction increases.
If we were able to reduce the effects of friction we could increase our speed and arrive sooner!
Train
Thrust
Weight
Normal Contact
Friction
Did you know?
The friction between wheels and rails in railways is called adhesive force.

## Slide 4
How do we reduce friction?
Using Magnetic Levitation!
40 min
London - Manchester

## Slide 5
The SCMaglev Train
S C Mag lev
uper
onducting
SCMaglev stands for...
netic
itation

## Slide 6
How fast can they go?
SMCMaglev stats:
World Record: 375mph (603km/h) Max Operation Speed: 311mph (500km/h)
Levitation: 10cm (4 inches)
Did you know?
Japan currently holds the world record in highest speed of crewed train!

## Slide 7
How they use Magnets
The lead vehicle (head car) weighs about 35 tons and the middle cars weighs about 25 tons.
In order to lift these heavy train cars, strong magnets need to be used.
These magnets are known as:
SCM: Super Conducting Magnets

## Slide 8
Electromagnets

## Slide 9
Current in a wire creates a magnetic field!
When current flows through a wire, the current generates a magnetic field around the wire!
The direction of the current determines
the direction of the poles.
Ampere’s right-hand rule!
Direction of current
Direction of Magnetic field

## Slide 10
Task 1: Draw the magnetic fields around the wires

## Slide 11
How do we make these magnets?
The magnetic field produced by a current flowing through a wire is very weak - too weak to be useful.
But...we can make it stronger!
Solenoids

## Slide 12
Solenoids
A solenoid is a long coil of insulated wire with current flowing through it.

## Slide 13
Task 2: Draw this
A solenoid produces a much stronger magnetic field than if the wire was straight.
The magnetic field is similar to that of a permanent magnet in some respects.
The field lines outside the solenoid form a complete loop inside.
The magnetic field inside the solenoid is strong and uniform. Many field lines and all in the same direction.

## Slide 14
The magnet can be made stronger by increasing the current
The heat could damage the components
Heat is generated by​
Electrical Resistance!
The higher the current, the more heat is generated

## Slide 15
So what should we do?
1 minute to discuss with the person next to you, before I choose people at random.

## Slide 16
Remove the resistance!
Strong current can be applied
The magnet can be strong!
Cool the coils to -269℃
No heat is generated

## Slide 17
What temperature are the coils kept at?
How long would it take a MagLev train to travel from London to Manchester?
Which hand & finger do we use to determine direction of current flowing
How would you increase the strength of an electromagnet
What is the main source of energy loss in electromagnetics
Learning check: Quick questions
Heat loss
Increase the current
Right Hand Thumb
40 minutes
-269℃
What is a Solenoid
Coiled wire carrying a current
1 minute to discuss with the person next to you, before I choose people at random.

## Slide 18
What is an Electromagnet?
An electromagnet is a solenoid (coil of wire with current flowing through it) with an iron core.
The iron core increases the strength of the magnetic field.

## Slide 19
How does a MagLev Train move forward?
Propelling the Train Forward
Nature of Magnets
Magnets have two poles; North and South
Repulsion between the same poles N and N or S and S
Attraction between opposite poles (N and S)

## Slide 20
The vehicle has magnets on each side.
There are four magnets in one box.
Four magnets
in one box

## Slide 21
Propelling the train forward
Nature of magnets
N-N or S-S : Repel
N-S : Attract

## Slide 22
Propelling the train forward
Which pole is
attracted by N?
S
Nature of magnets
N-N or S-S : Repel
N-S : Attract

## Slide 23
Propelling the train forward
S
Which pole is
attracted by S?
N
Nature of magnets
N-N or S-S : Repel
N-S : Attract

## Slide 24
Propelling the train forward
Ｎ
Ｓ
Ｎ
Ｓ
Ｎ
Ｎ
Ｓ
Ｓ
Ｎ
Ｓ

## Slide 25
Propelling the train forward
Ｎ
Ｓ
Ｎ
Ｓ
Ｎ
Ｎ
Ｓ
Ｓ
Ｎ
Ｓ

## Slide 26
Propelling the train forward

## Slide 27
Propelling the train forward

## Slide 28
Propelling the train forward

## Slide 29
Propelling the train forward

## Slide 30
Propelling the train forward

## Slide 31
Propelling the train forward

## Slide 32
Propelling the train forward

## Slide 33
Propelling the train forward

## Slide 34
Propelling the train forward

## Slide 35
Propelling the train forward

## Slide 36
Propelling the train forward

## Slide 37
Propelling the train forward

## Slide 38
Propelling the train forward
Let’s look at
one magnet on the ground!

## Slide 39
Propelling the train forward

## Slide 40
Propelling the train forward

## Slide 41
Propelling the train forward
Pole changed from S to N!

## Slide 42
Propelling the train forward

## Slide 43
Propelling the train forward
Pole changed from N to S!

## Slide 44
Propelling the train forward

## Slide 45
Propelling the train forward
Controlling vehicle movements by switching poles!

## Slide 46
Opposite poles ______.
How do we change the speed of the train?
Magnets are placed on the vehicle as well as the ______.
Learning check 2:
Quick questions
1 minute to discuss with the person next to you,
before I choose people at random.
Switching between poles accelerates or decelerates the vehicle.
Attract
Ground/rails.*
Like poles ______.
Repel
*Did you know? Maglev tracks are called guideways, not rails.

## Slide 47
Magnetic Field Around a Solenoid
Task 3: In-Depth Learning Check
Tasks:
What is a solenoid? [2 marks]
How can you tell the south pole of a solenoid? [1 mark]
Draw the magnetic field pattern for a solenoid, showing the direction of the field, and labelling the south and north pole. [3 marks]
Describe the magnetic field inside the solenoid and outside it. [3 marks]
How do we turn a solenoid into an electromagnet? [1 mark]
Challenge: What are the similarities and differences between the magnetic field of a solenoid and that of a bar magnet?

## Slide 48
A solenoid is a coil of wire (1) carrying an electrical current (1)​
The south pole would attract the north or repel another south pole (1)
One mark for lines running north to south; one mark for parallel lines in the centre; one mark for loop of magnetic field lines outside.
Task 3: Answers

## Slide 49
Task 3: Answers
The magnetic field inside the solenoid is strong and uniform (1)​
  Field lines inside are all in the same direction (parallel to the axis of the solenoid) (1)
  The field lines outside the solenoid are a complete loop (1)
Place an iron bar inside the coil / solenoid (1)

## Slide 50
Task 3: Answers
What are the similarities and differences between the magnetic field of a solenoid and that of a bar magnet?
Similarities
Both run N to S
Similar shape
Differences
The magnetic field outside the solenoid is similar to that of a (permanent) bar magnet, but not as strong (we can tell as there are fewer magnetic field lines).
The fewer lines of a solenoid are also a complete loop (i.e., inside the solenoid), unlike those of a bar magnet.

## Slide 51
Central Japan Railway Company’s original materials were adapted by Dylan Elliot Gentry in collaboration with The Japan Society to create this resource.
The Japan Society 13/14 Cornwall Terrace, London NW1 4QP
Tel: 020 7935 0475
Email: education@japansociety.org.uk
www.japansociety.org.uk
Follow us on:
@TheJapanSociety
@TheJapanSociety
© Original materials by Central Japan Railway Company, adapted by Dylan Elliot Gentry in collaboration with The Japan Society